## Slide 1: HPX-5 Throttling for Power
Livermore Unstructured Lagrangian Explicit Shock Hydrodynamics (LULESH)
Proxy application in DOE co-design efforts for exascale
CPU bounded in most implementations
Develop an APEX policy for power
  Threads are idled in HPX to keep node under power cap
  Use hysteresis of last 3 observations
  If Power < low cap increase thread cap
  If Power > high cap decrease thread cap
HPX thread scheduler modified to idle/activate threads per cap
Test example:
  343 domains, nx = 48, 100 iterations
  16 nodes of Edison, Cray XC30
  Baseline vs. Throttled (200W per node high power cap)
LULESH image, source: Hydrodynamics Challenge Problem, Lawrence Livermore National Laboratory. Technical Report, LLNL-TR-490254
Notes: LULESH is a proxy application from LLNL to model and study hydrodynamics, the motion of materials relative to each other when subject to forces.
The LULESH implementation was done by the researchers at IU.
We modified the thread scheduler algorithm to check the thread cap on every iteration of the main worker loop. If a thread is not holding any resources and the number of active workers is greater than the current thread cap, the thread goes into an idle state until signaled to resume work. If the number of active workers is less than the cap, an active worker signals an idle thread to resume working. The policy rule sets the thread cap according to the latest power observations. A quiescent node of Edison draws ~40W. Fully loaded, it draws ~300W.

## Slide 2: LULESH baseline
No power cap
No thread cap
768 threads
Avg. 247 Watts/node
~360 kiloJoules total
~91 seconds total
~74 seconds HPX tasks
Notes: The tasking time in the application takes ~74 seconds, when the aprun launch and HPX startup time is included, the total runtime is ~91 seconds. The read line shows the maximum concurrency, 768 threads (no cap used).The black line shows the cumulative power draw across all 16 nodes – it maxes out around 4500 W, about 281 W per node. The average power draw per node was around 247 W. The total energy usage was measured as 360 kiloJoules. The stacked bars show which tasks were executing when APEX sampled them with a 1Hz period (1 sample per second).

## Slide 3: LULESH Throttled by Power Cap
200W power cap
768 threads
throttled to 220
Avg. 186 Watts/node
~280 kiloJoules total
~94 seconds total
~77 seconds HPX tasks
Notes: This is the same measurement, with throttling enabled. The key difference: the total energy draw was only 280 kiloJoules, 22% less. The runtime only increased by ~3 seconds! The red line shows the thread cap as it is modified by the policy. The black line shows the reflected reduction in Power draw, with some localized fluctuations. The average power draw for this run was 186 W. This execution used less than 1/3 the number of threads, but only took 3 seconds longer. The next slide explains why…

## Slide 4: LULESH Performance Explanation
768 vs. 220 threads (after throttling)
360 kJ vs. 280 kJ total energy consumed (~22% decrease!)
75.24 vs. 77.96 seconds in HPX (~3.6% increase)
Big reduction in yielded action stalls (in thread scheduler) – fewer contention for locks
Total Task stats:
Metric | Baseline | Throttled | % Difference
Cycles | 1.11341E+13 | 3.88187E+12 | 34.865%
Instructions | 7.33378E+12 | 5.37177E+12 | 73.247%
L2 Cache Misses | 8422448397 | 3894908172 | 46.244%
IPC | 0.658677 | 1.38381 | 210.089%
INS/L2CM | 870.742 | 1379.18 | 158.391%
Notes: One big difference is that the throttled version of the code does not “yield” near as much as the original (I don’t have a good measurement of that yet). But a sampled profile showed much less time spent in yielding activity – when a worker thread surrenders its task to be executed by another worker. I don’t understand this phenomenon completely – I will have to talk to the IU people to fully understand what is happening, or why. The other big difference is reflected in the PAPI counters – the reduction in instructions is primarily due to the reduction in “yield” code. However, cache misses go way down, and instructions per L2 cache miss goes way up. The IPC is subsequently much higher due to the reduction in stall cycles.

## Slide 5
Much smaller example, 1 node.
48 threads, 64 domains, nx=25, i = 10
Time spent in “nop.S” based on sampling

## Slide 6
Thread 4 (2nd HPX worker thread),
Time spent in sampled functions

## Slide 7
Thread 4 (2nd HPX worker thread), Time spent in sampled lines